## Slide 1: SDN 路由
谢鲲

## Slide 2: 复杂多约束
路径受复杂多约束
  容量约束：链路上的占用带宽不得大于链路自身容量
  时延约束：端到端时延小于预定时延
  跳数约束：端到端跳数不能超过预定跳数
  必经约束：路径必须有序地经过某些节点和链路

## Slide 3: 生存性需求
抗故障路由设计需要为业务流寻找工作路径和保护路径，多条路径满足分离要求
  链路分离：工作与保护路径经过的链路互不相同
  节点分离：工作与保护路径经过的节点互不相同。节点分离必定链路分离。
  风险共享链路组（shared risk link group SRLG)分离：工作路径的风险共享链路组集合与保护路径的风险共享链路组集合没有交集
SRLG：具有同一故障风险的一个或者多个链路的集合。
一个链路可能属于多个SRLG。

## Slide 4: 多种优化目标
Min-min disjoint paths problem
Min-max disjoint paths problem
Bounded disjoint paths problem
Min-sum disjoint paths problem

## Slide 5: 难点分析
分离路径找不到
边冲突集合R：当第一条路径包含R时，第二条分离路径就找不到
        R={e1,e2}
发现和处理冲突集成为关键

## Slide 6: 研究内容
如何确定冲突集
如何设计Disjoint路由算法

## Slide 7: 如何确定冲突集
基于图转化来确定冲突集
星型SRLG分离的图形可以转换为边分离的图形
(a)
(b)
非星型SRLG
图如何处理？

## Slide 8: 如何确定冲突集
构图法来确定冲突集
如何构图?
如何确定冲突集？

## Slide 9: 如何设计路由算法
分而治之的并行路由
  得到边冲突集R，利用分而治之的思想，将原问题转换成更小的互斥的子问题，并行处理。
    P(I,O)表示路由问题：I：第一条路径必包含的边集合；O第一条路径必不包含的边集合
  冲突集|R|={e1,e2,…,e|T|}
    原问题可分解为下列子问题
      P(∅, {e1}), P( {e1}, {e2}),…, P({e1,e2,e3…e|T|-1},{e|T| }）
原问题
问题分解

## Slide 10: 如何设计路由算法
预处理
  节点转换为链路
  容量约束
复杂多约束
  满足多个可加路由指标是NP难
  拟转换多指标为单指标，如
路径约束
Notes: Suurballe’s algorithm

## Slide 11: 相关学术论文
Kun Xie, Xin Wang, Jigang Wen, Jiannong Cao, "Cooperative Routing with Relay Assignment in Multi-radio Multihop Wireless Networks", IEEE/ACM Transactions on Networking (TON), 2015(CCF A,SCI,DOI:10.1109/TNET.2015.2397035)
Kun Xie, Xin Wang, Xueli Liu, Jigang Wen, Jiannong Cao, Interference-aware Cooperative Communication in Multi-radio Multi-channel Wireless Networks, IEEE Transactions on Computers, 2015 (CCF A, SCI, DOI:10.1109/TC.2015.2448089)
Kun Xie, Jiannong Cao, Xin Wang, Jigang Wen. Optimal Resource Allocation for Reliable and Energy Efficient Cooperative Communications. IEEE Transactions on Wireless Communications, 2013,12(10),4994-5007 (CCF B, SCI)
Kun Xie, Ling Wang, Xueli Liu, Jigang Wen, Jiannong Cao, Cooperative Routing with Relay Assignment in Multi-radio Multi-hop Wireless Networks, IWQoS2014 (CCF B, acceptance ratio of 23.8%)
He Shiming, Zhang Dafang, Xie Kun, Qiao Hong, Zhang ji. Channel Aware Opportunistic Routing in Multi-radio Multi-channel Wireless Mesh Network. Journal of Computer Science and Technology, 2014, 29(3): 487-501 (SCI,CCF B类)
Hong Qiao, Dafang Zhang, Kun Xie, Ji Zhang, Shiming He, A Distributed Joint Cooperative Routing and Channel Assignment in Multi-radio Wireless Mesh Network, ICA3PP 2015 (CCF C)
Kun Xie*, Hui Li, Xin Wang, Shiming He, Jigang Wen, Mohsen Guizani. Routing and Channel Assignment in Wireless Cooperative Networks. IWCMC 2014(acceptance ratio of 34%)
Kun Xie, Ye Liu, Jigang Wen, Shiming He. CVMIMOR: Cooperative Virtual MIMO Routing in Wireless Networks. International Journal of Wireless and Mobile Computing, 2014,7(2),171-179
谢鲲,段申琳,文吉刚,何施茗.基于博弈的协作路由算法,通信学报, 2013, 34(z1):44-57(学科国内重点期刊)

## Slide 12: 相关学术论文
乔宏，张大方，谢鲲，何施茗，张继.分布式多网关无线mesh网公平协作路由算法.通信学报.2015,36(2):1~11(学科国内重点期刊)
Shiming He, Dafang Zhang, Kun Xie, Ji Zhang, Hong Qiao. Opportunistic Routing for Multiple Multicast flows in Wireless Mesh Networks. International Journal of Wireless and Mobile Computing, 2014,17(1),84-92
Shiming He, Dafang Zhang, Kun Xie, Ji Zhang, Hong Qiao. JORCA: Joint Opportunistic Routing and Channel Assignment. International Journal of Embedded Systems, 2014,6( 2/3): 148-158
何施茗,张大方,谢鲲,张继,乔宏.多并发流无线网状网中的机会路由算法. 电子学报. 2014,42(5):1004-1008 (学科国内重点期刊)
Shiming He, Dafang Zhang, Kun Xie, Ji Zhang, Hong Qiao. Joint Opportunistic Routing Selection and Channel Assignment in multi-radio multi-channel WMNs. EUC-2013
Shiming He, Dafang Zhang, Kun Xie, Xiaan Bi, Hong Qiao, ji Zhang, and Bin Zeng.A Candidate Forwarder Set based Channel Assignment for opportunistic routing in Multi-Radio Wireless Mesh Networks. CWSN2012
Shiming He, Dafang Zhang, Kun Xie, Hong Qiao and Ji Zhang. A Distributed Low-complexity Channel Assignment for Opportunistic Routing. China Communications. 2012.11,9-22 (SCI)
Ji Zhang, Dafang Zhang, Kun Xie, Shiming He, Hong Qiao, and BinZeng. A Cooperative Routing Algorithm for Maximizing Network Lifetime. CWSN2012
He Shiming, Zhang Dafang, Xie Kun, Qiao Hong, Zhang ji. "A Simple Channel Assignment for Opportunistic Routing in Multi-Radio Multi-Channel Wireless Mesh Networks". MSN 2011
乔宏,张大方*,谢鲲,何施茗,张继.多射频无线mesh网中的联合协作路由与信道分配算法,电子学报，已录用(学科国内重点期刊)
张继,张大方*,谢鲲,何施茗,乔宏,一种基于演化博弈的分簇协作路由算法,电子学报，已录用(学科国内重点期刊)

## Slide 13: 谢谢！